## Slide 1
Fingerspelling Recognition with Two-Steps Cascade Process of
Spotting and Classification
Masanori Muroi1, Naoya Sogi1, Nobuko Kato2, Kazuhiro Fukui1
1 Graduate School of Systems and Information Engineering, University of Tsukuba, Japan
2 Faculty of Industrial Technology, Tsukuba University of Technology, Japan
(1) Introduction
Fingerspelling is a tool to express proper nouns and new technical terms that have not been yet defined in sign languages.
Main goal : Detect and recognize fingerspellings in an input video which is composed of fingerspellings and not fingerspelling signs.
Basic idea : Divide a whole process into two-steps cascade process:
  Spotting : Extract a fingerspelling sequence in an input video by utilizing temporal dynamic information.
  Classification : Classify the spotted sequence by utilizing 3D hand shape information.
To efficiently incorporate two different information, we propose a fingerspelling classification framework
based on three methods: 1) temporal regularized CCA (TRCCA)[1] for spotting, 2) orthogonal mutual subspace method (OMSM)[2] and 3) CNN features[3] for classification.
We proposed fingerspelling recognition framework based on a complementary combination of TRCCA and OMSM with CNN features.
We confirmed that our two-steps process significantly outperforms conventional one-step methods in terms of classification accuracy and recognition time.
Step1: Spotting process
Step2: Classification process
Dataset:
  We recorded 15 fingerspelling classes by a depth camera.
  We synthesized an input video, which continuously inputs fingerspelling and not fingerspelling sequences alternately.
Evaluation index:
  Spotting performance, Classification accuracy, Recognition time.
Sample images of our fingerspelling dataset.
(2) Proposed framework
(3) Experiments
Confusion Matrix: Results of the spotting process.
Confusion Matrix:
Results of the classification process
Accuracies and recognition times of different methods.
Framework | Accuracy | Recognition Time
TRCCA[1] | 64.1% | 39.7 ms
CNN feat - OMSM | 68.9% | 52.7 ms
KOTRCCA[1] | 79.0% | 169.0 ms
TRCCA - CNN(softmax) | 80.7% | 56.9 ms
TRCCA - KOMSM | 86.9% | 187.3 ms
TRCCA - CNN feat - OMSM(Proposed) | 88.2% | 91.2 ms
(4) Conclusion
[1]S. Tanaka, A. Okazaki, N. Kato, H. Hino and K. Fukui, Spotting fingerspelled words from sign language video by temporally regularized canonical component analysis, 2016 IEEE International Conference on Identity, Security and Behavior Analysis, 2016, pp. 1-7.
[2]K. Fukui and O. Yamaguchi, The kernel orthogonal mutual Subspace method and its application to 3D object recognition, in Asian Conference on Computer Vision, 2007, pp. 467-476.
[3] N. Sogi, T. Nakayama, and K. Fukui, A method based on convex cone model for image-set classification with cnn features, in 2018 International Joint Conference on Neural Networks, 2018, pp. 1-8.
(5) References
Japanese fingerspelling examples
Static
Dynamic
“a”
“mo”
Fingerspelling images in an input video are detected by considering the temporal information using TRCCA.
TRCCA: Calculate similarity between two sequences
considering temporal information.
The detailed procedure
1.1 The input image sequence is compared with
the reference fingerspelling by TRCCA.
If the input sequence has high similarity with the reference
fingerspelling, the input sequence is classified as a fingerspelling.
1.2 Fingerspelling images are extracted
from the input sequence.
Spotted fingerspelling is classified by OMSM with CNN features using hand shape image sets.
OMSM: Represent 3D shape of a hand by subspace,
then classify it by subspace similarity.
The detailed procedure
2.1 CNN features and are extracted from and .
2.2 Each class subspace and an input subspace are generated by applying PCA
to the sets of CNN features.
2.3 Orthogonal subspaces { and are generated by applying orthogonalize
transformation to .
2.4 The spotted fingerspelling is classified based on similarities between the input subspace
and reference subspaces {.